## Slide 1: Energy-efficient system providing superior IAQ
3fficiency: pinnacle, NEUTON and chilled beams

## Slide 2: 3fficiency system components
3fficiency™ is the “Pinnacle” of chilled beam systems. The 3 components included in the system package are:
Pinnacle™ Dedicated Outside Air System (DOAS),
NEUTON™ Chilled Beam Pump Module, and
SEMCO Active Chilled Beam line.
The NEUTON pump module manages the water system to allow for a building level occupant control that is superior to all other systems.

## Slide 3: 3fficiency system

## Slide 4: System Configuration
Feature set includes:
1. The outside air portion of the system will be treated by a Pinnacle
2. Each zone has a combination of:
  a. A chilled beam
  b. Diffuser
  c. Return grill
  d. Temp and humidity sensor
  e. Opt 2 way valve (if multiple zones are required)
3. Each 1-5 zones will have a NEUTON (See Figure 1)
4. Controls are all native Bacnet

## Slide 5: Direct Replacement for VRF
3fficiency can directly replace Variable Refrigerant Flow (VRF)
Provides even more savings through the use of a water to water chiller and using the condenser water as the hot water for the system
No more concerns with ASHRAE 15, refrigerant leaks, or large electrical wire runs
A whole building Variable WATER Flow System!

## Slide 6: CHILLED BEAMS
Active and Passive

## Slide 7: Passive Chilled Beams
The << engine >> is the gravity and the density difference between the cold air and the warm air
Only cooling mode
The air diffusion isn’t controlled and there are risks of draft below the chilled beam
Passive chilled beams are used only for an additional source of cooling for a specific need.

## Slide 8: Active Chilled Beams
The « engine » is the induction created by the adjustable slots.
Cooling and heating mode.
The fresh air is supplied through the chilled beam.
Mixing air diffusion into the room so the air velocity is controlled.
Active chilled beams provide heating, cooling and ventilation with high comfort.

## Slide 9: Active Chilled Beams

## Slide 10: Comfort Control
Adjustable induction on site
Different air distribution available:
  One way distribution
  Two way distribution
  Asymmetric air diffusion
Chilled beam capacity can be increased or decreased by slot adjustment
No tools required
50%
50%
80%
20%
0%
100%

## Slide 11: IQHC Air Slider Label

## Slide 12: IQHC Air Slider Open

## Slide 13: IQHC Air Slider Half Open

## Slide 14: IQHC Air Slider Closed

## Slide 15: Universal Beams

## Slide 16: Flow Pattern Control System
Plastic blades to adjust air diffusion & throw length Angles: 0°- 15°- 30°- 45°
Modules of 2 feet to get different flow pattern
Manual adjustment from room to room, no tools required
        Increased comfort level
        Flexibility in building design
        No tools required

## Slide 17: Bottom Closed

## Slide 18: Bottom Open

## Slide 19: Accessories for Installation
Attachment QFAZ-18
Attachment CB-IQHC-24
        Faster installation
        Easier installation
Installation cost reduction
Fastening Brackets for both types of installation:
Free hanging installation
False ceiling installation

## Slide 20: Chilled Beams Benefits
Experience
Applied in Europe for more than 3 decades
Applied in the US more than 10 years
SEMCO manufactured in the United States for more than 5 years
Indoor Air Quality
Increased ventilation to each space (all applications)
Better air distribution (circulation) within the space
Lower sound levels than almost all HVAC systems
Energy Savings
Reduced fan horsepower
Load matching (only use space cooling if required)
Higher temperature chilled water (increased chiller efficiency)
First Cost Savings
Reduced duct size
Reduced interstitial space
Smaller air handlers, plant rooms

## Slide 21: NEUTON
Controlled Chilled Beam Pump Module
U.S. patent number 9,625,222

## Slide 22: Concept
42 oF

## Slide 23: Component Parts
Integrated electrical, DDC controls panel
Electronically Commutated Motor (ECM) high efficiency, variable speed pump
Hot water control valve
Chilled water control valve
Chilled water return
Hot water supply
Zone loop return connection
Chilled water supply
Hot water return
Zone supply water connection
Pete’s plugs for pressure and flow measurement
Zone supply water thermistor
Pump Isolation Valves
ZS Pro Sensor Zone Controller
NEUTON Chilled Beam Pump Module

## Slide 24: How It Works: (4 pipe primary loop)

## Slide 25: NEUTON Benefits
New Construction:
Reduction of installation cost by 30% and more
Use of conventional water (chilled/hot)
Simplifies installation, and includes zone level controls
Active condensation control
Reduces pump energy and addresses load matching
Improves response to occupied/unoccupied conditions
PATENTED DESIGN: U.S. patent number 9,625,222
Existing Construction:
Re-utilize existing hot water / chilled water systems piping and central plant
Alleviates concern regarding vapor barrier (or lack thereof)
True energy savings compared to VRF option
  Similar design
  Reduces refrigerant

## Slide 26: Traditional 4 Pipe Approach

## Slide 27: Unconventional 2 Pipe Approach

## Slide 28: Main Loop View
PUMPS SIZED FOR MAIN LOOP WITH REGARD TO TOTAL GPM REQUIRED AND PRESSURE VARIABLE SPEED OF PUMP CONTROLELD BASED ON THERMOWELL DESIGNATED DELTA TEMP
WATER IN BOTH LOOPS HAVE TO HAVE SAME CHEMISTRY
CHILLED WATER PUMP
HOT WATER PUMP
HOT WATER BOILER
HEAT EXCHANGER TO ISOLATE BEAM LOOP FROM CENTRAL PLANT

## Slide 29: Greatly simplify Design and Installation Process
Factory wired/tested
Zone Pump
Water temp sensor
Control Valve
Electrical/controls
Electrical Field connections required
Smart sensor
Main power (208/230 – 1 Ph)
BAS (if applicable)
Water connections
6 pipe connections
Swivel half-union adapters
Designed for std 1” male fitting

## Slide 30: Vertical or Horizontal Mounting Accommodated
Notes:
NEUTON can be mounted in several positions as long as the pump shaft remains horizontal (as shown above)
Adequate space must be allocated of opening the hinged panel door and accessing the DDC control board and other components

## Slide 31: Room Smart Sensor
Features
Full digital display
Communicates with NEUTON via BACnet
Wall sensor includes:
Temperature
Relative Humidity
CO2 (optional)

## Slide 32: Reduced First Cost Comparison
Estimated Installed Cost | SOA 4 Pipe Coils | NEUTON 4 Pipe Coils | NEUTON 2 Pipe Coils
Primary Loop | $65,000 | $23,840 | $10,450
Zone Loops, Beams, Controls, NEUTON | $68,230 | $77,300 | $77,300
Total Installed Cost (1) | $133,230 | $101,140 | $87,750
Reduction from SOA Baseline (percentage) | 0% | 24% | 34%
Reduction from SOA Baseline ($/sq.ft.) | $0 / sq.ft. | $2.10 / sq.ft. | $3.00 / sq.ft.
Note 1: Includes all installed components except ductwork and Pinnacle DOAS equipment and installation |  |  | 
Summary of Zone Performance/Cost Analysis: Current State-of-the-Art 4-Pipe Approach vs. NEUTON and 2-Pipe Approach

## Slide 33: System integration
PINNACLE – NEUTON - CHILLED BEAMS

## Slide 34: Space Humidity Remains Regardless of Location
BTUH
Based on 0.04% ASHRAE Peak Dry Bulb Design

## Slide 35: Space Humidity Remains Regardless of Location
Based on 0.04% ASHRAE Peak Dewpoint Design
BTUH

## Slide 36: What Determines Minimum Primary Airflow?
ASHRAE 62 minimum ventilation requirement
Minimum to satisfy space latent load
Minimum to satisfy space sensible load
Make-up air requirement
*Laboratory, Kitchen Exhaust Make-up, Etc.

## Slide 37: How Supply Dewpoint Effects Primary Airflow
Maintaining 50% space relative humidity at 75F db
Based on 3 ton space latent load

## Slide 38: Pinnacle Dual Wheel DOAS - Review
Outdoor Air
Cooling Coil
Supply Air
SEMCO TE
Total Energy Wheel
(Pressure loss)
0.83 in.wg.
SEMCO PD
Passive DH Wheel
(Pressure loss)
0.82 in.wg.
11,813 CFM
95.0°db
/
78.0°wb
118.1 gr
41.4 BTU/lb
10,818 CFM
77.3°db
/
68.3°wb
89.6 gr
32.6 BTU/lb
10,818 CFM
52.5°db
/
52.1°wb
57.2 gr
21.5 BTU/lb
10,000 CFM
61.2°db
/
52.5°wb
45.0 gr
21.8 BTU/lb
9,000 CFM
75.0°db
/
62.5°wb
65.0 gr
28.3 BTU/lb
10,813 CFM
89.3°db
/
75.3°wb
109.9 gr
38.7 BTU/lb
TE Purge/Seals (995 CFM)
9,818 CFM
67.6°db
/
62.9°wb
78.6 gr
28.5 BTU/lb
PD Purge/Seals (818 CFM)
Exhaust Air
0.72 in.wg.
(Pressure loss)
(PD Wheel Speed
.25 RPM)
Return Air
0.793
TE Effectiveness
0.73 in.wg.
(Pressure loss)

## Slide 39: Summarizing Primary Air and Humidity Concern
Traditional beam system approach utilizes higher dewpoint/colder air
Primary benefit of chilled beam system is horsepower reduction
To maximize energy benefit, minimize primary air
Lower the airflow, the lower the dewpoint required.
Application type impacts approach – 3fficiency system can be adjusted to suit the application and amount of outdoor air required

## Slide 40: Occupancy Impacts Primary Air
Chilled Beams require ½ the airflow of a traditional VAV system design

## Slide 41: Energy Modeling: Systems Compared
Energy modeling completed for an actual High School project comparing three design approaches which highlights the significant fan and pump energy savings offered by the 3fficiency system.

## Slide 42: System Integration Summary
Geography doesn’t eliminate humidity concerns
Lower dewpoints requires lower primary airflow requirement
A Pinnacle unit uses the lowest dewpoint with the least energy
Primary Air is determined by
  ASHRAE 62
  Minimum Dehumidification
  Minimum Sensible
  Make up air requirement
Adjustable nozzles makes test and balance easier
A chilled beam system can save more than 50% of the building’s HVAC energy
3fficiency uses an average of 70% less pump energy to achieve better comfort than traditional equipment

## Slide 43: competition
DUAL WHEEL DEHUMIDIFIERS

## Slide 44: Competitor #1 – Peak Dry Bulb
Total Energy Wheel
Passive DH Wheel
(Pressure loss)
(Pressure loss)
0.80 in.wg.
1.27 in.wg.
Cooling Coil
1.27 in.wg.
(Pressure loss)
(PD Wheel Speed RPM) – 0.61
0.797
TE Effectiveness
0.70 in.wg.
(Pressure loss)
81.3°db
/
67.7°wb
10,538 CFM
80.2 gr
32.1 BTU/lb
57.0°db
/
50.7°wb
10,000 CFM
45.0 gr
20.7 BTU/lb
51.0°db
/
51.0°wb
20.8 BTU/lb
10,538 CFM
55.6 gr
77.3°db
/
68.5°wb
90.8 gr
10,538 CFM
32.8 BTU/lb
93.5°db / 76.0°wb
10,366 CFM
107.9 gr
38.5 BTU/lb
95.0°db / 78.0°wb
11,366 CFM
118.1 gr
41.4 BTU/lb
81.3°db
/
67.7°wb
10,538 CFM
80.2 gr
32.1 BTU/lb
75.0°db
/
62.5°wb
9,000 CFM
65.0 gr
28.2 BTU/lb
50%
Outdoor Air
Return Air
Supply Air
Exhaust Air

## Slide 45: Competitor #1 – Part Load
61%
Total Energy Wheel
Passive DH Wheel
(Pressure loss)
(Pressure loss)
0.80 in.wg.
1.27 in.wg.
70.0°db
/
70.0°wb
74.5°db
/
65.1°wb
74.5°db
/
65.1°wb
71.8°db
/
65.8°wb
Cooling Coil
73.4°db
/
69.4°wb
75.0°db
/
62.5°wb
55.7°db
/
51.0°wb
51.0°db
/
51.0°wb
0.797
1.27 in.wg.
TE Effectiveness
(Pressure loss)
0.70 in.wg.
(PD Wheel Speed RPM) – 0.61
(Pressure loss)
10,538 CFM
78.2 gr
30.1 BTU/lb
85.6 gr
20.8 BTU/lb
10,000 CFM
48.2 gr
20.8 BTU/lb
10,538 CFM
55.6 gr
11,366 CFM
110.8 gr
10,538 CFM
30.6 BTU/lb
10,366 CFM
102.1 gr
33.6 BTU/lb
34.1 BTU/lb
10,538 CFM
78.2 gr
30.1 BTU/lb
9,000 CFM
65.0 gr
28.2 BTU/lb
Outdoor Air
Return Air
Supply Air
Exhaust Air

## Slide 46: Competitor #1 – Part Load
61%
Total Energy Wheel
Passive DH Wheel
(Pressure loss)
(Pressure loss)
0.80 in.wg.
1.27 in.wg.
70.0°db
/
70.0°wb
74.5°db
/
65.1°wb
74.5°db
/
65.1°wb
71.8°db
/
65.8°wb
Cooling Coil
73.4°db
/
69.4°wb
75.0°db
/
62.5°wb
55.7°db
/
51.0°wb
51.0°db
/
51.0°wb
0.797
1.27 in.wg.
TE Effectiveness
(Pressure loss)
0.70 in.wg.
(PD Wheel Speed RPM) – 0.61
(Pressure loss)
10,538 CFM
78.2 gr
30.1 BTU/lb
85.6 gr
20.8 BTU/lb
10,000 CFM
48.2 gr
20.8 BTU/lb
10,538 CFM
55.6 gr
11,366 CFM
110.8 gr
10,538 CFM
30.6 BTU/lb
10,366 CFM
102.1 gr
33.6 BTU/lb
34.1 BTU/lb
10,538 CFM
78.2 gr
30.1 BTU/lb
9,000 CFM
65.0 gr
28.2 BTU/lb
Solution #1
Colder Coil
PROBLEM WILL BE COLDER DISCHARGE
Outdoor Air
Return Air
Supply Air
Exhaust Air

## Slide 47: Competitor #1 – Part Load
Solution #2
Add Heating
Total Energy Wheel
Active DH Wheel
(Pressure loss)
Heating Coil
(Pressure loss)
0.80 in.wg.
1.27 in.wg.
70.0°db
/
70.0°wb
74.5°db
/
65.1°wb
81.3°db
/
67.3°wb
77.3°db
/
68.0°wb
Cooling Coil
73.4°db
/
69.4°wb
75.0°db
/
62.5°wb
57.0°db
/
50.6°wb
51.0°db
/
51.0°wb
0.797
1.27 in.wg.
TE Effectiveness
(Pressure loss)
0.70 in.wg.
(PD Wheel Speed RPM) – 0.61
(Pressure loss)
10,538 CFM
78.2 gr
31.8 BTU/lb
88.2 gr
20.8 BTU/lb
10,000 CFM
44.6 gr
20.6 BTU/lb
10,538 CFM
55.6 gr
11,366 CFM
110.8 gr
10,538 CFM
32.4 BTU/lb
10,366 CFM
102.1 gr
33.6 BTU/lb
34.1 BTU/lb
10,538 CFM
78.2 gr
30.1 BTU/lb
9,000 CFM
65.0 gr
28.2 BTU/lb
Outdoor Air
Return Air
Supply Air
Exhaust Air

## Slide 48: Competitor #2 – Peak Dry Bulb
Outside air jumps over return air path
Total Energy Wheel
Active DH Wheel
Heating Coil
(Pressure loss)
1.27 in.wg.
95.0°db
/
78.0°wb
93.5°db
/
76.0°wb
125.0°db
/
67.3°wb
108.0°db
/
82.9°wb
81.3°db
/
67.7°wb
75.0°db
/
62.5°wb
58.0°db
/
57.0°wb
77.0°db
/
58.8°wb
1.27 in.wg.
Cooling Coil
(Pressure loss)
(PD Wheel Speed RPM) – 0.61
(Return Side Pressure)
(Supply Side Pressure)
0.80 in.wg.
0.797
TE Effectiveness
0.70 in.wg.
9,828 CFM
107.9 gr
31.8 BTU/lb
130.9 gr
25.5 BTU/lb
10,538 CFM
68.0 gr
24.5 BTU/lb
10,000 CFM
45.0 gr
11,366 CFM
118.1 gr
10,366 CFM
46.7 BTU/lb
10,538 CFM
80.2 gr
32.1 BTU/lb
41.4 BTU/lb
9,828 CFM
107.9 gr
39.5 BTU/lb
9,000 CFM
65.0 gr
28.2 BTU/lb
18%
Supply Temp Adds Load to Space
Outdoor Air
Supply Air
Exhaust Air
Return Air

## Slide 49: Competitor #2 – Part Load
30%
Total Energy Wheel
Active DH Wheel
Heating Coil
(Pressure loss)
1.27 in.wg.
70.0°db
/
70.0°wb
73.4°db
/
69.4°wb
104.9°db
/
78.0°wb
89.9°db
/
77.3°wb
74.5°db
/
65.1°wb
75.0°db
/
62.5°wb
58.0°db
/
57.0°wb
75.0°db
/
59.5°wb
1.27 in.wg.
Cooling Coil
(Pressure loss)
(PD Wheel Speed RPM) – 0.61
(Return Side Pressure)
(Supply Side Pressure)
0.80 in.wg.
0.797
TE Effectiveness
0.70 in.wg.
9,828 CFM
102.1 gr
41.4 BTU/lb
122.1 gr
26.0 BTU/lb
10,538 CFM
68.0 gr
24.5 BTU/lb
10,000 CFM
48.0 gr
11,366 CFM
110.8 gr
10,366 CFM
40.8 BTU/lb
10,538 CFM
78.2 gr
30.1 BTU/lb
34.1 BTU/lb
9,828 CFM
102.1 gr
33.6 BTU/lb
9,000 CFM
65.0 gr
28.2 BTU/lb
Outdoor Air
Supply Air
Exhaust Air
Return Air

## Slide 50: Competitor #2 – Part Load
Total Energy Wheel
Active DH Wheel
Heating Coil
(Pressure loss)
1.27 in.wg.
70.0°db
/
70.0°wb
73.4°db
/
69.4°wb
104.9°db
/
78.0°wb
89.9°db
/
77.3°wb
74.5°db
/
65.1°wb
75.0°db
/
62.5°wb
58.0°db
/
57.0°wb
75.0°db
/
59.5°wb
1.27 in.wg.
Cooling Coil
(Pressure loss)
(PD Wheel Speed RPM) – 0.61
(Return Side Pressure)
(Supply Side Pressure)
0.80 in.wg.
0.797
TE Effectiveness
0.70 in.wg.
9,828 CFM
102.1 gr
41.4 BTU/lb
122.1 gr
26.0 BTU/lb
10,538 CFM
68.0 gr
24.5 BTU/lb
10,000 CFM
48.0 gr
11,366 CFM
110.8 gr
10,366 CFM
40.8 BTU/lb
10,538 CFM
78.2 gr
30.1 BTU/lb
34.1 BTU/lb
9,828 CFM
102.1 gr
33.6 BTU/lb
9,000 CFM
65.0 gr
28.2 BTU/lb
Solution #1
Colder Coil
30%
Outdoor Air
Supply Air
Exhaust Air
Return Air

## Slide 51: Competitor #2 – Part Load
Solution #2
Hotter Coil
Total Energy Wheel
Active DH Wheel
Heating Coil
(Pressure loss)
1.27 in.wg.
70.0°db
/
70.0°wb
73.4°db
/
69.4°wb
125.0°db
/
82.8°wb
108.0°db
/
77.3°wb
74.5°db
/
65.1°wb
75.0°db
/
62.5°wb
58.0°db
/
57.0°wb
77.0°db
/
58.8°wb
1.27 in.wg.
Cooling Coil
(Pressure loss)
(PD Wheel Speed RPM) - 0.61
(Return Side Pressure)
(Supply Side Pressure)
0.80 in.wg.
0.797
TE Effectiveness
0.70 in.wg.
9,828 CFM
102.1 gr
46.4 BTU/lb
125.1 gr
25.5 BTU/lb
10,538 CFM
68.0 gr
24.5 BTU/lb
10,000 CFM
45.0 gr
11,366 CFM
110.8 gr
10,366 CFM
45.8 BTU/lb
10,538 CFM
78.2 gr
30.1 BTU/lb
34.1 BTU/lb
9,828 CFM
102.1 gr
33.6 BTU/lb
9,000 CFM
65.0 gr
28.2 BTU/lb
Outdoor Air
Supply Air
Exhaust Air
Return Air

## Slide 52: SEMCO Pinnacle
Total Energy Wheel
Passive DH Wheel
(Pressure loss)
Cooling Coil
(Pressure loss)
0.80 in.wg.
0.82 in.wg.
95.0°db
/
78.0°wb
74.0°db
/
66.8°wb
51.3°db
/
50.9°wb
62.0°db
/
52.8°wb
88.5°db
/
75.0°wb
63.1°db
/
60.7°wb
75.0°db
/
62.5°wb
TE Purge/Seals
(828 CFM)
PD Purge/Seals
(538 CFM)
0.797
0.72 in.wg.
TE Effectiveness
(Pressure loss)
0.70 in.wg.
(PD Wheel Speed RPM) –
0.61
(Pressure loss)
10,538 CFM
54.7 gr
20.8 BTU/lb
45.0 gr
28.2 BTU/lb
9,538 CFM
75.7 gr
26.9 BTU/lb
9,000 CFM
65.0 gr
11,366 CFM
118.1 gr
10,000 CFM
21.9 BTU/lb
10,366 CFM
109.5 gr
38.5 BTU/lb
41.4 BTU/lb
10,538 CFM
87.5 gr
31.4 BTU/lb
Outdoor Air
Return Air
Supply Air
Exhaust Air
50%

## Slide 53: SEMCO Pinnacle
Cooling Coil
95.0°db
/
78.0°wb
74.0°db
/
66.8°wb
51.3°db
/
50.9°wb
62.0°db
/
52.8°wb
88.5°db
/
75.0°wb
63.1°db
/
60.7°wb
75.0°db
/
62.5°wb
Total Energy Wheel
(Pressure loss)
0.80 in.wg.
0.797
TE Effectiveness
0.70 in.wg.
(Pressure loss)
10,538 CFM
54.7 gr
20.8 BTU/lb
45.0 gr
28.2 BTU/lb
9,538 CFM
75.7 gr
26.9 BTU/lb
9,000 CFM
65.0 gr
11,366 CFM
118.1 gr
10,000 CFM
21.9 BTU/lb
10,366 CFM
109.5 gr
38.5 BTU/lb
41.4 BTU/lb
10,538 CFM
87.5 gr
31.4 BTU/lb
OUTDOOR DEPENDENT
Passive DH Wheel
(Pressure loss)
0.82 in.wg.
0.72 in.wg.
(Pressure loss)
(PD Wheel Speed RPM) -
0.61
Outdoor Air
Return Air
Supply Air
Exhaust Air
50%
TE Purge/Seals
(828 CFM)
PD Purge/Seals
(538 CFM)

## Slide 54: SEMCO Pinnacle
Cooling Coil
95.0°db
/
78.0°wb
74.0°db
/
66.8°wb
51.3°db
/
50.9°wb
62.0°db
/
52.8°wb
75.0°db
/
62.5°wb
Total Energy Wheel
(Pressure loss)
0.80 in.wg.
0.797
TE Effectiveness
0.70 in.wg.
(Pressure loss)
10,538 CFM
54.7 gr
20.8 BTU/lb
45.0 gr
28.2 BTU/lb
9,000 CFM
65.0 gr
11,366 CFM
118.1 gr
10,000 CFM
21.9 BTU/lb
41.4 BTU/lb
10,538 CFM
87.5 gr
31.4 BTU/lb
50%
Passive DH Wheel
(Pressure loss)
0.82 in.wg.
0.72 in.wg.
(Pressure loss)
(PD Wheel Speed RPM) -
0.61
Outdoor Air
Return Air
Supply Air
Exhaust Air
OUTDOOR DEPENDENT
SPACE DEPENDENT
88.5°db
/
75.0°wb
10,366 CFM
109.5 gr
38.5 BTU/lb
TE Purge/Seals
(828 CFM)
63.1°db
/
60.7°wb
9,538 CFM
75.7 gr
26.9 BTU/lb
PD Purge/Seals
(538 CFM)

## Slide 55: SEMCO Pinnacle – Part Load
Cooling Coil
70.0°db
/
70.0°wb
67.1°db
/
64.2°wb
51.3°db
/
50.9°wb
62.0°db
/
52.8°wb
68.6°db
/
68.3°wb
63.1°db
/
60.7°wb
75.0°db
/
62.5°wb
Passive DH Wheel
(Pressure loss)
0.82 in.wg.
0.72 in.wg.
(Pressure loss)
(PD Wheel Speed RPM) -
0.61
Total Energy Wheel
(Pressure loss)
0.80 in.wg.
0.797
TE Effectiveness
0.70 in.wg.
(Pressure loss)
10,538 CFM
54.7 gr
20.8 BTU/lb
45.0 gr
28.2 BTU/lb
9,538 CFM
75.7 gr
26.9 BTU/lb
9,000 CFM
65.0 gr
11,366 CFM
110.8 gr
10,000 CFM
21.9 BTU/lb
10,366 CFM
103.7 gr
32.6 BTU/lb
34.1 BTU/lb
10,538 CFM
85.5 gr
29.4 BTU/lb
50%
Outdoor Air
Return Air
Supply Air
Exhaust Air
TE Purge/Seals
(828 CFM)
PD Purge/Seals
(538 CFM)

## Slide 56: SEMCO Pinnacle – Part Load
Cooling Coil
70.0°db
/
70.0°wb
67.1°db
/
64.2°wb
51.3°db
/
50.9°wb
62.0°db
/
52.8°wb
68.6°db
/
68.3°wb
63.1°db
/
60.7°wb
75.0°db
/
62.5°wb
Passive DH Wheel
(Pressure loss)
0.82 in.wg.
0.72 in.wg.
(Pressure loss)
(PD Wheel Speed RPM) -
0.61
Total Energy Wheel
(Pressure loss)
0.80 in.wg.
0.797
TE Effectiveness
0.70 in.wg.
(Pressure loss)
10,538 CFM
54.7 gr
20.8 BTU/lb
45.0 gr
28.2 BTU/lb
9,538 CFM
75.7 gr
26.9 BTU/lb
9,000 CFM
65.0 gr
11,366 CFM
110.8 gr
10,000 CFM
21.9 BTU/lb
10,366 CFM
103.7 gr
32.6 BTU/lb
34.1 BTU/lb
10,538 CFM
85.5 gr
29.4 BTU/lb
50%
Outdoor Air
Return Air
Supply Air
Exhaust Air
TE Purge/Seals
(828 CFM)
PD Purge/Seals
(538 CFM)

## Slide 57: SEMCO Pinnacle – Part Load
Cooling Coil
70.0°db
/
70.0°wb
67.1°db
/
64.2°wb
51.3°db
/
50.9°wb
62.0°db
/
52.8°wb
68.6°db
/
68.3°wb
63.1°db
/
60.7°wb
75.0°db
/
62.5°wb
Total Energy Wheel
(Pressure loss)
0.80 in.wg.
0.797
TE Effectiveness
0.70 in.wg.
(Pressure loss)
10,538 CFM
54.7 gr
20.8 BTU/lb
45.0 gr
28.2 BTU/lb
9,538 CFM
75.7 gr
26.9 BTU/lb
9,000 CFM
65.0 gr
11,366 CFM
110.8 gr
10,000 CFM
21.9 BTU/lb
10,366 CFM
103.7 gr
32.6 BTU/lb
34.1 BTU/lb
10,538 CFM
85.5 gr
29.4 BTU/lb
50%
Passive DH Wheel
(Pressure loss)
0.82 in.wg.
0.72 in.wg.
(Pressure loss)
(PD Wheel Speed RPM) -
0.61
Outdoor Air
Return Air
Supply Air
Exhaust Air
OUTDOOR DEPENDENT
SPACE DEPENDENT
TE Purge/Seals
(828 CFM)
PD Purge/Seals
(538 CFM)

## Slide 58: 3fficiency – QUESTIONS?
3fficiency™ is the “Pinnacle” of chilled beam systems. The 3 components included in the system package are:
  Pinnacle™ Dedicated Outside Air System (DOAS),
  NEUTON™ Chilled Beam Pump Module, and
  SEMCO Active Chilled Beam line.
NEUTON is what makes 3fficiency™ possible.
QUESTIONS?